CS401

Assignment#1_Solution

Question No. 1:

a)

Suppose your computer has a processor with 24-bit address lines. What is maximum amount of memory that can be attached in your system? (Show the step(s) for calculation of maximum addressable memory) (2.5 marks)

Solution: -

Accessible memory addresses = 2number of address bits

224 = 16777216 bytes

16777216 / 1024 = 16384 KB

16384 / 1024 = 16 MB

b)

How many address bits are required for accessing 1GB RAM? (Show the step(s) for calculation of required address bits) (2.5 marks)

Solution: -

As you know 1GB means 1024MB so we can write it as

1GB = 1024 x 1MB

As you know that 1MB is 220

So we can write the expression as

1024 x 220

This can be further simplified as

210 x 220

=230

Hence, 30 address lines are required to access 1GB RAM.

Question No. 2:

What are the contents of memory locations 0151, 0152, 0153, ………….,0158 if 0151 is starting address for Label1. (1 mark for each location)

Label1:	dw	8494

db	42

dw	54

dw	7500

db	01

Solution: -

| Memory location | Contents |
| --- | --- |
| 0151 | 94 |
| 0152 | 84 |
| 0153 | 42 |
| 0154 | 54 |
| 0155 | 00 |
| 0156 | 00 |
| 0157 | 75 |
| 0158 | 01 |

Question No. 3:

a)

Calculate physical address using the following segment offset pairs. (1 mark each)

- 00EA:02A4

- 0100:AA23

- D3B8:F222

- 00A0:1234

- 8FEf:0FFF

Solution: -

1)

00EA0

002A4 +

_______

01144   = physical address

2)

01000

0AA23 +

_______

0BA23   = physical address

3)

D3B80

0F222 +

_______

E2DA2   = physical address

4)

00A00

01234 +

________

01C34   = physical address

5)

8FEF0

00FFF +

_________

90EEF   = physical address

b)

What is effective address generated by the following instructions? Every instruction is independent of others. Initially bx = 0x0101, bp=0x0222, si=0x1234, var1=0x1771

(1 mark each)

- mov ax, [bx+si]

- mov ax, [bx+100] (100 is in decimal)

- mov ax, [bp+si]

- mov ax, [var1+bp]

- mov ax, [si+var1]

Solution: -

1)

Effectice address = [bx+si]

= [0101 + 1234]

= [1335]

2)

Effectice address = [bx + 100]

After converting 100 into hexadecimal

Effectice address = [bx + 64]

= [0101 + 64]

= [0165]

3)

Effective address = [bp+si]

= [0222 + 1234]

= [1456]

4)

Effective address = [var1+bp]

= [1771 + 0222]

= [1993]

5)

Effective address = [si + var1]

= [1234 + 1771]

= [29A5]