|  | Assignment No. 04 Semester: Spring 2011 CS401: Computer Architecture and Assembly Language Programming | Total Marks: 20 Due Date:23rd June, 2011 |
| --- | --- | --- |
| Instructions Please read the following instructions carefully before submitting assignment: It should be clear that your assignment will not get any credit if: The assignment is submitted after due date. The submitted assignment does not open or file is corrupt. Solution is copied from any other source. Note: You have to submit your assignment in Ms word (.doc file) format. Assignment in any other format (extension) will not be accepted. Objective The objective of this assignment is to enhance your knowledge about Multitasking concepts in Assembly language Understand and modify existing Assembly code |
| Assignment |  |
| This assignment is based upon Elementary multitasking of two threads Example 11.1 given in Lectures handouts. Given code in example 11.1 creates two simple threads each rotating bars by changing characters at the two corners of the screen and have infinite loops. Its output looks like as below: Figure 1: Output of Example 11.1 in Lectures handouts, having TWO threads shown in RED circles. You are required to Modify the given code in Example 11.1 such that it creates THREE threads each rotating bars by changing characters have infinite loops at Left corner, Center and Right corners of the screen respectively. Its output MUST looks like as below: Figure 2: Required output having THREE threads running, shown in RED circles. Submission: Submit your modified Assembly Program code in Ms Word format by clearly Highlighting instructions you have Added/Modified. (10 Marks) Explain briefly the purpose of instructions you Added/Modified.(05 Marks) In Example 11.1 program, there is an instruction (Single) through which we can control the No. of threads running i.e. by modifying that instruction we can execute one or more thread among existing as we wish. Identify that instruction. (05 Marks) |
| NOTE: You have to use and modify Example 11.1. Any other program will not be accepted, even if it has the desired output. You must submit your solution through LMS within due date. No assignment would be accepted through email after deadline. |
| Solution: ; elementary multitasking of three threads [org 0x0100] jmp start ; ax,bx,ip,cs,flags storage area taskstates: dw 0, 0, 0, 0, 0 ; task0 regs dw 0, 0, 0, 0, 0 ; task1 regs dw 0, 0, 0, 0, 0 ; task2 regs dw 0, 0, 0, 0, 0 ; task3 regs current: db 0 ; index of current task chars: db '\¦/-' ; shapes to form a bar ; one task to be multitasked taskone: mov al, [chars+bx] ; read the next shape mov [es:0], al ; write at top left of screen inc bx ; increment to next shape and bx, 3 ; taking modulus by 4 jmp taskone ; infinite task ; second task to be multitasked tasktwo: mov al, [chars+bx] ; read the next shape mov [es:158], al ; write at top right of screen inc bx ; increment to next shape and bx, 3 ; taking modulus by 4 jmp tasktwo ; infinite task ; Third task to be multitasked taskthree: mov al, [chars+bx] ; read the next shape mov [es:70], al ; write at top right of screen inc bx ; increment to next shape and bx, 3 ; taking modulus by 4 jmp taskthree ; infinite task ; timer interrupt service routine timer: push ax push bx mov bl, [cs:current] ; read index of current task mov ax, 10 ; space used by one task mul bl ; multiply to get start of task mov bx, ax ; load start of task in bx pop ax ; read original value of bx mov [cs:taskstates+bx+2], ax ; space for current task pop ax ; read original value of ax mov [cs:taskstates+bx+0], ax ; space for current task pop ax ; read original value of ip mov [cs:taskstates+bx+4], ax ; space for current task pop ax ; read original value of cs mov [cs:taskstates+bx+6], ax ; space for current task pop ax ; read original value of flags mov [cs:taskstates+bx+8], ax ; space for current task inc byte [cs:current] ; update current task index cmp byte [cs:current], 4 ; is task index out of range jne skipreset ; no, proceed mov byte [cs:current], 0 ; yes, reset to task 0 skipreset: mov bl, [cs:current] ; read index of current task mov ax, 10 ; space used by one task mul bl ; multiply to get start of task mov bx, ax ; load start of task in bx mov al, 0x20 out 0x20, al ; send EOI to PIC push word [cs:taskstates+bx+8] ; flags of new task push word [cs:taskstates+bx+6] ; cs of new task push word [cs:taskstates+bx+4] ; ip of new task mov ax, [cs:taskstates+bx+0] ; ax of new task mov bx, [cs:taskstates+bx+2] ; bx of new task iret ; return to new task start: mov word [taskstates+10+4], taskone ; initialize ip mov [taskstates+10+6], cs ; initialize cs mov word [taskstates+10+8], 0x0200 ; initialize flags mov word [taskstates+20+4], tasktwo ; initialize ip mov [taskstates+20+6], cs ; initialize cs mov word [taskstates+20+8], 0x0200 ; initialize flags mov word [taskstates+30+4], taskthree ; initialize ip mov [taskstates+30+6], cs ; initialize cs mov word [taskstates+30+8], 0x0200 ; initialize flags mov word [current], 0 ; set current task index xor ax, ax mov es, ax ; point es to IVT base cli mov word [es:8*4], timer mov [es:8*4+2], cs ; hook timer interrupt mov ax, 0xb800 mov es, ax ; point es to video base xor bx, bx ; initialize bx for tasks sti jmp $ ; infinite loop |

# Comments

To hold task3 Registers

Code of Task3 running in infinite loop.

This instruction control No. of running threads. By setting its value 4 will include third Task execution.

Populate task3 registers with Task3 addresses.