|  | Assignment No. 04 Semester Spring 2011 Advance Computer Architecture - CS501 | Total Marks: 15 Due Date: 19/06/2011 |
| --- | --- | --- |
| Objective: To learn and understand basic concepts of I/O subsystems, and DMA Instructions: Please read the following instructions carefully before solving & submitting assignment: Assignment should be in your own wordings not copied from net, handouts or books. It should be clear that your assignment will not get any credit (zero marks) if: The assignment is submitted after due date. The submitted assignment does not open or file corrupt. The assignment is copied (from other student or copy from handouts or internet). Student ID is not mentioned in the assignment File or name of file is other than student ID. GOOD LUCK |
| Q:1 An I/O device transfers data at a rate of 5MB/s over a 100MB/s bus. The data is transferred in 2KB blocks. If the processor operates at 500MHz, and it takes a total of 5000 cycles to handle each DMA request, find the fraction of CPU time handling the data transfer with and without DMA. [10] Solution. Without DMA The processor here copies the data into memory as it is sent over the bus. Since the I/O device sends data at a rate of 5MB/s over the 100MB/s bus, 5 % of each second is spent transferring data. Thus 5% of the CPU time is spent copying data to memory. With DMA Time required in handling each DMA request is 5000 cycles. Since 2500 DMA requests are issued (5MB/2KB) the total time taken is 12,500,000 cycles. As the CPU clock is 500MHZ, the fraction of CPU time spent is 12,500,000/(500x106) or 2.5%. Q:2 A 4 K byte block of data is read from a disk drive. What is the overall data transmission rate if the disk drive has a latency of 7 ms, and a burst bandwidth of 2 MB per second? [5] Solution: Total time = (4 K / 2 MB *103 ms) + 7 ms = 9 ms Overall transmission rate = 4 K / 9 ms = 0.44 MB/s |